## Slide 1
MIRAJ JUNCTION RAILWAY STATION

## Slide 2: MIRAJ CITY
SITE LOCATION
MAHARASHTRA
SANGLI
Miraj Railway Station
Bus Connectivity
MIRAJ Bus Stand
Airport Connectivity
KOLHAPUR AIRPORT Airport
Distance - 52.7 kms
1 Hr 20 minutes
Tourist Places to Visit Near By
Miraj MARKET
Ganesh Talav
Sangli Fort : 10 kms
Sagareshwar Wildlife Sanctuary : 56 kms
Audumbar Lord Datta Temple : 34 kms
Baliraja Agro Tourism
Distance - 500 m
3 minutes
Time -
Time -
CONNECTIVITY TO MIRAJ RAILWAY STATION

## Slide 3: MIRAJ CITY DEMOGRAPHICS
ABOUT THE CITY
Miraj is a city in Sangli District, southern Maharashtra, India, that was founded in the early 10th century.
The city is recognised for Hindustani classical music and Medical services.
Many medical tourists visit from adjoining districts of North Karnataka and from Arab countries.
Maximum Temperature - 43 °C Minimum Temperature - 6.5 °C
680 mm of rainfall per year.
Humidity is: 82.0%
POPULATION
2021(Estimated)
4,36,217
LITERACY RATE
ELEVATION
AREA
118 km2
549 m
85.93%
WIND SPEED
6 KM/hr
Miraj Railway Station
Sangli District
Climate

## Slide 4: EXISTING MIRAJ JUNCTION RAILWAY STATION
Kavanthe mahankal miraj road (SH-137)
Miraj road
Maniknagar Bypass (3m wide)
YASHWANTPUR
PUNE
KOLHAPUR
MIRAJ JUNCTION
STATION RD
RAILWAY LINE
ROADS
MIRAJ BUS STAND
MIRAJ BUS DEPOT
KAVANTE
Internal road
N

## Slide 5: EXISTING MIRAJ JUNCTION RAILWAY STATION – ROAD CONNECTIVITY
STATION ROAD
INTERNAL ROAD-01
INTERNAL ROAD-02
INTERNAL ROAD-03
INTERNAL ROAD-04
MANIKNAGAR BYPASS
MAIN ROAD/ INTERNAL ROADS
ENCROACHED /BLOCKED PART OF ROAD (NO VEHICLE ENTRY POSSIBLE)
MIRAJ JUNCTION
MIRAJ BUS STAND
INTERNAL ROAD
N

## Slide 6: EXISTING CIRCULATION, PARKING AND INFRASTRUCTURE
KAVATHE MAHANKAL MIRAJ ROAD
STATION ROAD
FOB 1
FOB 2
MANIKNAGAR BYPASS
MIRAJ BUS DEPOT
MIRAJ BUS STAND
ROB
PLATFORM 2
PLATFORM 3
PLATFORM 4
PLATFORM 5
PLATFORM 6
MIRAJ BUS STAND
BUS STAND CIRCULATION RAILWAY STATION CIRCULATION
UNDER CONSTRUCTION RAIL. BUSINESS JUNCTION MALL
AUTO PARKING
RAILWAY STATION
PLATFORM 1
ACCESSIBILITY
Railway station is accessed from east side only.
FOB connects the East and West side.
PARKING
2 wheeler parking, 4 wheeler parking available at east side of station.
BUS STOP
Miraj Bus stand is 500 m away from the railway station .
No bus stop along the rear side of the railway station.
KUNKESHWAR- TALEWADI ROAD
N

## Slide 7: EXISTING CIRCULATION & PARKING
RAILWAY STATION
PARCEL OFFICE
RMS OFFICE
2 WHEELER PARKING
TAXI PARKING
AUTO PARKING
PARCEL BUILDING DROP OFF
AREA OF CONGESTION
FOB 2
FOB 1
EXISITNG PARKING
AUTO PARKING - 30 TAXI PARKING - 15
2 WHEELER PARKING - 100
Segregation of lanes not done
Designated parking not provided
Drop off & Pick up lanes not defined
Departureand arrival not segregated
STATION ROAD
1
2
4
3

## Slide 8: EXISTING MIRAJ RAILWAY STATION (ENTRANCE EAST SIDE)

## Slide 9: EXISTING MIRAJ RAILWAY STATION
RESERVATION CENTRE
TICKET COUNTER

## Slide 10: MIRAJ RAILWAY STATION : PLATFORMS
PLATFORM 6
PLATFORM 5
PLATFORM 4
PLATFORM 3
PLATFORM 2
14 M
10 M
3
KEY PLAN

## Slide 11: EXISTING STATION PLATFORM

## Slide 12
MIRAJ RAILWAY STATION : PLATFORMS
MIRAJ RAILWAY STATION : PLATFORMS
SINGLE LANE MANIKNAGAR BYPASS

## Slide 13: KEY ISSUES WITH THE EXISTING STATION
NO CONTINUOUS TRAFFIC LOOP FOR VEHICLES. STATION ROAD ENDS AT STATION AND VEHICLES TAKE “U” TRUN FOR RETURN CAUSING CONGESSION.
NO DEDICATED PARKING FOR 2W/4W/AUTO OUTSIDE STATION.
NO STATION BUILDING ON WEST SIDE CAUSING LACK OF DEVELOPMENT THERE.
NO SEGRAGATION OF ARRIVING AND DEPARTING PASSENGERS.
ABSENCE OF LIFTS AND ELEVATORS FOR THE FOB.
INADEQUATE PUBLIC AMENITIES LIKE WAITING/SITTING AREAS AND TOILETS ETC.
THE ARCHITECTURAL RESPONSE TO BE COGNIZANT WITH THE ARCHITECTRUAL HERITAGE OF MIRAJ.

## Slide 14
INSPIRED BY GANESH TEMPLE, NEAR MIRAJ
ARCHITECTURE OF PATWARDHAN PALACE

## Slide 15: PASSENGER FOOTFALL
0
2000000
4000000
6000000
8000000
10000000
12000000
14000000
2020
2030
2040
2050
2060
12574000
PER DAY PASSENGER PEAK HOUR
- 23,140
- 2300 (approx)
EXISTING DATA
2020-21 TOTAL ANNUAL FOOTFALL - 84,46,000
PROJECTED FOOTFALL FOR YEAR 2060
2060 TOTAL ANNUAL FOOTFALL – 1,25,74,000
PER DAY PASSENGER PEAK HOUR
- 34,448
- 3400 (approx)
11384000
10306000
9330000
8446000
NOTES: 1% ANNUAL GROWTH IN PASSENGER FOOTFALL IS CONSIDERED FOR FUTURE FOOTFALL CALCULATION.

## Slide 16: PASSENGER FOOTFALL
sr.no. | Estimation of floor areas for station building/ Departure Concourse- MIRAJ RAILWAY STATION |  |  |  |  |  | 
1 | Horizon year | 2020 | 2030 | 2040 | 2050 | 2060 | Mela Surge @ 35%
2 | Passenger data | Area units ( SQ .M.) |  |  |  |  | 
2.1 | Average Annual day - Peak hour passenger demand (a) | 1160 | 1276 | 1404 | 1544 | 1698 | 2293
2.2 | Average Annual day - Peak hourDeparture passenger demand (b)** 55% of total peak hour passenger | 638 | 702 | 772 | 849 | 934 | 1261
2.3 | Average Annual day - Peak hourArrivalpassenger demand ©**45% of total peak hour Passenger | 522 | 574 | 632 | 695 | 764 | 1032
2.4 | Average annual day passenger demand per day (d) | 11600 | 12760 | 14036 | 15440 | 16984 | 22928
2.5 | Level of service envisaged | A | A | B | C | C | D
2.6 | Departure passenger - Waiting for more than 30 mins ** 40% of total peak hour passenger | 255 | 281 | 309 | 340 | 374 | 504
Yearly chart - Projected Passenger footfall |  |  |  |  | 
 | 2020 | 2030 | 2040 | 2050 | 2060
Peak Hour Passenger | 2300 | 2550 | 2820 | 3120 | 3400

## Slide 17: PASSENGER FOOTFALL
3 | Check in Queue Space for20%of total Peak hourDeparturepassengers (b) / Security Check |  |  |  |  |  | 
3.1 | Standard (sq.m./person) for check in queue space | 1.71 | 1.71 | 1.53 | 1.35 | 1.35 | 1.35
3.2 | Space Required (sq.m.) | 218 | 240 | 236 | 229 | 252 | 340
4 | Wait/circulate space for20%oftotal Peak hourDeparturepassengers |  |  |  |  |  | 
4.1 | Level of service envisaged | A | A | B | C | C | D
4.2 | Standard (sq.m./person) for wait/circulate space | 2.61 | 2.61 | 2.25 | 1.8 | 1.8 | 1.44
4.3 | CIRCULATION Space Required (sq.m.) | 333 | 366 | 347 | 306 | 336 | 363
5 | Waiting Area |  |  |  |  |  | 
5.1 | Level of service envisaged | A+ (3 SQ M) | A+ (3 SQ M) | A+ (3 SQ M) | A+ (3 SQ M) | A+ (3 SQ M) | B (2.25 SQ M)
5.2 | Wait area forExecutive class 5 % of peak passengers (e) | 38 | 42 | 46 | 51 | 56 | 142
5.3 | Level of service envisaged | A(2.61 SQ M) | A(2.61 SQ M) | A(2.61 SQ M) | A(2.61 SQ M) | A(2.61 SQ M) | B(2.25 SQ M)
5.4 | Wait area for 1st AC @ 10 % of peak passengers (f) | 67 | 73 | 81 | 89 | 98 | 132
5.5 | Level of service envisaged | B(2.25 SQ M) | B(2.25 SQ M) | B(2.25 SQ M) | B(2.25 SQ M) | B(2.25 SQ M) | C(1.8 SQ M)
5.6 | Wait area for2ND & 3RD AC @ 35 % of peak Departure passengers (g) | 201 | 221 | 243 | 267 | 294 | 318
5.7 | Level of service envisaged | C(1.8 SQ M) | C(1.8 SQ M) | C(1.8 SQ M) | C(1.8 SQ M) | C(1.8 SQ M) | D(1.44 SQ M)
5.8 | Wait area for SLEEPER & UNRESERVED 50 % of peak Departure passengers (h) | 230 | 253 | 278 | 306 | 336 | 363
5.9 | TOTAL AREA FOR WAITING (e+f+g+h) | 536 | 589 | 648 | 713 | 784 | 954

## Slide 18: PASSENGER FOOTFALL
6 | Hold room for 30% of totalDeparturePeak hour passengers |  |  |  |  |  | 
6.1 | Standard (sq.m./person) for hold room space | 1.4 | 1.35 | 0.99 | 0.99 | 0.99 | 0.99
6.2 | Space Required (sq.m.) | 258 | 284 | 229 | 252 | 277 | 375
7 | Arrival lobbyfor10 % of totalArrivalPeak hour passengers |  |  |  |  |  | 
7.1 | Level of service envisaged | A | A | B | C | C | C
7.2 | Standard (sq.m./person) for lobby | 1.7 | 1.71 | 1.53 | 1.35 | 1.35 | 1.35
7.3 | Space Required (sq.m.) | 89 | 98 | 97 | 94 | 103 | 139
7.4 | Wait/circulate space for 20% oftotal Peak hourArrivalpassengers |  |  |  |  |  | 
7.5 | Level of service envisaged | A | A | B | C | C | C
7.6 | Standard (sq.m./person) for wait/circulate space | 2.61 | 2.61 | 2.25 | 1.8 | 1.8 | 1.8
7.7 | CIRCULATION Space Required (sq.m.) | 272 | 300 | 284 | 250 | 275 | 371
8 | Total Space required for check in queue + wait/circulate + Waiting areas | 1449 | 1593 | 1612 | 1592 | 1751 | 2169

## Slide 19: 3D VIEWS

## Slide 20: VIEW FROM STATION MAIN ENTRY (EAST SIDE)

## Slide 21: VIEW OF DEPARTURE GATE (EAST SIDE)
Miraj is known for historical and religious significance as well as cultural heritage.
It is also known for its rich tradition of classical music ,dance and theatre.

## Slide 22: AERIAL VIEW OF STATION ENTRY

## Slide 23: AERIAL VIEW OF STATION DROP-OFF AREA (EAST SIDE)

## Slide 24: VIEW OF STATION FACADE (EAST SIDE)

## Slide 25: VIEW OF STATION FACADE (EAST SIDE)

## Slide 26: VIEW FROM MAIN ACCESS ROAD (EAST SIDE)

## Slide 27: VIEW OF DEPARTURE GATE (EAST SIDE)

## Slide 28: VIEW OF PEDESTRIAN CROSSING (EAST SIDE)

## Slide 29: VIEW OF STATION ARRIVAL GATE (EAST SIDE)

## Slide 30: VIEW OF STATION ARRIVAL GATE (EAST SIDE)

## Slide 31: AERIAL VIEW FROM STATION (WEST SIDE)

## Slide 32: VIEW FROM STATION ENTRY (WEST SIDE)

## Slide 33: VIEW OF WEST SIDE STATION

## Slide 34: VIEW OF PEDESTRIAN CROSSING (WEST SIDE)

## Slide 35: AERIAL VIEW OF STATION DROP-OFF AREA (WEST SIDE)

## Slide 36: AERIAL VIEW OF STATION

## Slide 37: MASTER PLAN

## Slide 38: PROPOSED MASTER PLAN
105M
105M

## Slide 39: FLOOR PLANS

## Slide 40: GROUND LEVEL PLAN (PLATFORM LEVEL)
24 M

## Slide 41: +5.5M LEVEL PLAN (INTERMEDIATE LEVEL)

## Slide 42: +9 M LEVEL PLAN (CONCOURSE LEVEL)
24 M WIDE PASSAGE
24 M

## Slide 43: DEPARTURE CONCOURSE LAYOUT
DN TO PLATFORM
DN TO PLATFORM
DN TO PLATFORM
DN TO PLATFORM
DN TO PLATFORM
DN TO PLATFORM
DN TO PLATFORM
DN TO PLATFORM
80M
24M
24 M WIDE CONCOURSE

## Slide 44: STATION LAYOUT PLAN OF EAST SIDE
Station Layout At Platform Level
Station Layout At +9m Level
Station Layout At +5.5m Level
ARRIVAL BLOCK-1
DEPARTURE BLOCK
ARRIVAL BLOCK-2
ARRIVAL BLOCK-1
KEY PLAN

## Slide 45: STATION LAYOUT PLAN OF WEST SIDE
Station Layout At Platform Level
Station Layout At +5.5m Level
KEY PLAN
Station Layout At +9m Level

## Slide 46: AREA STATEMENT
SN | Items | No of floors | Area in Sqm (East + West) | Size (length x Width) |  | Remarks
1 | Area of Development (Station building + Concourse + Connecting bridges ) | G+2 | 17165 |  |  | 
 |  |  | East Side Terminal 9775 | 238M x 21 M Arrival block 1– 85M x13M Arrival block 2-65M x22M Departure Block 1- 90M x 18M |  | 
 |  |  | West Side Terminal 1800 | 60M x 10M |  | 
2 | Station Building | Platform level | 3975 |  |  | 
 |  | At +5.5 Level | 3315 |  |  | 
 |  | At +9 Level | 4300 |  |  | 
3 | Air concourse | Departure Concourse (24M Wide) At +9 Level | 1850 |  |  | 
 |  | 2 No. Arrival Bridges (6M Wide) At +9 Level | 3000 |  |  | 
 |  | Connecting Bridges At +9 Level | 725 |  |  | 
4 | Roof,covering and platform areas | Station Main Roof | 7000 |  |  | 
 |  | Connecting Bridge coverings (Arrival air concourse+ departure connecting bridge) | 2900 |  |  | 
 |  | Platform covering | 14000 |  |  | 
 |  | Platform Refurbishment | 22000 |  |  | 
5 | Surface parking | East Side terminal- 100 (2W), 25 (auto) and 20(4W) | 1580(EAST SIDE) 1000 (WEST SIDE) |  |  | 
 |  | West Side terminal- 20 (4W), 40 (2W) and 20 (auto) |  |  |  | 
6 | No of platforms | 6 |  |  |  | 
7 | Escalators | 23 (+9M LVL) 01(+5.5 M LVL) |  |  |  | 
8 | Lift | 23 |  |  |  | 
9 | FOBS | Proposed 2 No. Arrival Bridges (6M Wide) At +9 Level and 1 existing | 250 (extension), 500 (renovation) |  |  | 
10 | MLCP | NA |  |  |  | 

## Slide 47: ESTIMATE
PROPOSED MANDATORY AREAS- NORTH SIDE
REDEVELOPMENT OF MIRAJ JUNCTION RAILWAY STATION |  |  |  | 
ABSTRACT OF COST ESTIMATE |  |  |  | 
SL No | PACKAGES | Area (sqm) | TOTAL AMOUNT (INR) | Rate/ Sq.m
 | RAILWAY INFRASTRUCTURE DEVELOPMENT |  |  | 
1 | STATION BUILDING |  |  | 
 | MAIN BUILDING (East Side + West Side) | 11590 | 69,54,00,000 | 60,000
2 |  |  |  | 
 | MAIN ROOF |  |  | 
3 | Aluminium Double seem standing roof with Insulation - Roofing system | 7,000 | 24,50,00,000 | 35,000
4 | DEPARTURE CONCOURSE BLOCK | 1850 | 13,32,00,000 | 72,000
5 | ARRIVAL CONCOURSE & CONNECTING BRIDGE BLOCK | 3725 | 24,58,50,000 | 66,000
6 | EXISTING PLATEFORMS DEVELOPMENT |  |  | 
 | ROOFING & FLOORING | 36,000 | 28,80,00,000 | 8,000
7 | CONNECTING BRIDGE COVERING COST | 3725 | 5,58,75,000 | 15,000
8 | RAILWAY OFFICE BUILDING (G+2)+ ORH | 1,884 | 9,42,08,000 | 50,000
9 | EXTERNAL DEVELOPMENT |  | 10,00,00,000 | 
10 | LIFT & ESCALATORS |  | 25,00,00,000 | 
11 | INTERNAL & EXTERNAL SIGNAGES (INCLUDING ROAD DIRECTIONS OVER ELEAVTED ROAD & DIGITAL SIGNANGES AT ALL APPROPRIATE LOCATIONS) |  | 1,50,00,000 | 
12 | ART WORK (Lumpsum ) |  | 5,00,00,000 | 
13 | STREET FURNITURE INCLUDING FURNITURE FOR DEPARTURE CONCOURSE , RAILWAY OFFICES ETC |  | 1,00,00,000 | 
14 | MEP High Side |  | 15,00,00,000 | 
15 | PROVISIONAL COST OF UTILITY SHIFTING |  | 5,00,00,000 | 
 | Golf Cart 2Nos |  | 16,00,000 | 
 | High Mast 20M High 2Nos |  | 50,00,000 | 
 | TOTAL FOR STATION DEVELOPMENT (GST inclusive) |  | 238,91,33,000 | 
A | D & G Charges @ 5.32% |  | 12,71,07,875 | 
1 | Add : Contengies @ 1% |  | 2,38,91,330 | 
 | Add : Design Charge @ 1% |  | 2,38,91,330 | 
 | Total Cost (A) |  | 256,40,23,535 | 
B | DEMOLITION OF PART STATION BUILDING, BRIDGE RAILWAY QUARTERS (Amount to be credited ) 1 Cr Lumsum |  | 1,00,00,000 | 
 | Miscellaneous |  |  | 
 | G.TOTAL (A-B) |  | 257,40,23,535 | 
 | AMOUNT IN CR. |  | 257.4 | 

## Slide 48: RELOCATION STAGES

## Slide 49: RELOCATION STAGE - 1
STAGE-1
Office building and staff house will be demolished and temp provision will be made in existing station building at first floor.
NEW CONSTRUCTED STRUCTURE DEMOLISHED STRUCTURE EXISTING STATION BUILDING
EXISTING STATION BUILDING
REST
HOUSE
U/C

## Slide 50: RELOCATION STAGE - 2
STAGE-3
Part of the existing station building to be demolished in this stage and facilities there to be shifted to arrival hall-01 at intermediate level.
b. For remaining facilities, temporary arrangement to be done on rent.
NEW CONSTRUCTED STRUCTURE DEMOLISHED STRUCTURE EXISTING STATION BUILDING
EXISTING STATION BUILDING
Arrival Hall -01
West side station building
6M WIDE ARRIVAL FOB

## Slide 51: RELOCATION STAGE - 3
STAGE-4
Departure hall, Departure concourse and connecting bridge to the west side station building to be constructed in this stage.
NEW CONSTRUCTED STRUCTURE DEMOLISHED STRUCTURE EXISTING STATION BUILDING
PART EXISTING STATION BUILDING
Arrival Hall -01
West side station building
Departure Hall
24M WIDE DEPARTURE CONCOURSE
6M WIDE ARRIVAL FOB
6M WIDE CONNECTING BRIDGE

## Slide 52: RELOCATION STAGE - 4
STAGE-5
Remaining part of existing station building to be demolished in this stage and facilities there to be shifted to newly constructed departure hall at platform level and intermediate level.
NEW CONSTRUCTED STRUCTURE DEMOLISHED STRUCTURE EXISTING STATION BUILDING
PART EXISTING STATION BUILDING
Arrival Hall -01
Departure Hall
24M WIDE DEPARTURE CONCOURSE
6M WIDE ARRIVAL FOB
6M WIDE CONNECTING BRIDGE
West side station building

## Slide 53: RELOCATION STAGE - 5
STAGE-6
Arrival hall-02 and FOB-02 to be constructed in this stage.
NEW CONSTRUCTED STRUCTURE DEMOLISHED STRUCTURE EXISTING STATION BUILDING
Arrival Hall -01
Departure Hall
24M WIDE DEPARTURE CONCOURSE
6M WIDE ARRIVAL FOB-01
Arrival Hall -02
6M WIDE ARRIVAL FOB-02
West side station building

## Slide 54
3D VIEWS
OPTION-2

## Slide 55
VIEW OF STATION DROP-OFF AREA

## Slide 56
VIEW OF STATION ENTRY

## Slide 57
AERIAL VIEW OF STATION ENTRY

## Slide 58
VIEW OF CONCOURSE

## Slide 59
VIEW OF CONCOURSE

## Slide 60
3D VIEW
AERIAL VIEW OF STATION

## Slide 61
3D VIEWS
OPTION-03 (COLONNADE THEME)
.

## Slide 62
VIEW-01

## Slide 63
VIEW-02

## Slide 64
VIEW-03

## Slide 65
VIEW-04

## Slide 66
VIEW-05

## Slide 67
VIEW-06

## Slide 68: THANK YOU

## Slide 69: EXTRACT OF FACTS
DIRECTION: EAST(MAIN) & West
TOTAL BUILTUP AREA: 17165 sq.m.(E+W)
(Terminal buildings + Air concourse
+Connecting bridge)
SURFACE PARKING (E+W) : 50(4W) +150(2W) + 50 (Auto rickshaw)
DEPARTURE CONCOURSE: 24MX80M (600 SEATING CAPACITY)
ARRIVAL CONCOURSE WIDTH: 6M
TOTAL COST: 257 CR
PASSENGER DEMAND (PEAK) 2300 (2020) 3400 (2060)
LOS ENVISAGED A(2020-40) B(2040-50) C(2050-60)